## Slide 1: EE 152 – Real-time embedded systems
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Lab 7: Pan-Tompkins-Charles algorithm

## Slide 2: Today’s problem
Given an ECG:
  Find the QRS complex
  Compute the heart rate (HR)

## Slide 3: First-try algorithm
Find the peaks (using a derivative)
Peak at >1v  QRS
Then HR is easy
Problems?
  Everyone’s voltage is different
1V

## Slide 4: Algorithm v2
Get running high and low peaks over 10 seconds
Threshold = low + .9*(high-low) / 2
Any peak > threshold  QRS
Any problems with algorithm v2?
high
low
threshold

## Slide 5
60Hz noise turns one peak into two peaks
Ideas?
  Don’t accept two peaks “close” to each other
Chart: one cycle of an ECG, zoomed out
Chart: zoomed in
 | 2182 | 2229 | 2272 | 2312 | 2329 | 2353 | 2381 | 2400 | 2456 | 2491 | 2520 | 2529 | 2525 | 2530 | 2476 | 2436 | 2405 | 2375 | 2341 | 2292 | 2241
Notes: This comes from OA.

## Slide 6: RBBB
RBBB ECG typically has two distinct peaks
  First is the small partial peak from RBB conduction
  Next is the bigger peak from LBB wraparound
  Can easily show up as two peaks
Chart: RBBB, 500 samples/sec
Notes: This is from my la_ra_normal1, but inverted.
I’ve no idea why it always shows up in green.

## Slide 7: Baseline drift
SHOW A BASELINE DRIFT ECG
Drift may be too fast for the algorithm to keep up
high
low
threshold

## Slide 8: Algorithm v3
Get running high and low peaks over 10 seconds
Threshold = (low + high) / 2
Any peak > threshold  QRS except if it’s in the lockout period
How do we set the lockout period?
Max HR of a 20 year old  200 beats/minute
  200 beats/minute = 60 sec/200 beat = .3 sec/beat
  So lockout for, say, .25 sec after any QRS
Does it work now?
In-class exercise
Notes: Well, the double peak on my ECG is separated by about 25 samples at 2ms/sample, or 50ms. So a .25sec lockout will work fine on my ECG, at least.

## Slide 9: Weird ECGs
Show a tall P or T giving a fast HR
Exercise on your own: will lockout fix this?
Onto the “real” algorithm

## Slide 10: Pan Tompkins Charles
1985: Jiapu Pan and Willis Tompkins published original algorithm
2023 Charles modified it for this course (unpublished)
  Working as an independent study
  Used Joel’s ECG, and got it to work just before the summer ended

## Slide 11: PTC idea #1
Keep the running min peak & max peak
Each new peak of height h
    min_peak = min (min_peak, h)
    max_peak = max (max_peak, h)
    thresh = (min_peak + max_peak) / 2
Every 2ms
    min_peak += delta
    max_peak -= delta
This one is from C (PT had a different scheme)

## Slide 12: PTC idea #2
Work in two tracks
  Track #1 is what we described. And track #2 is…
QRS is not only tall, but also pointy
  “Pointy” means high slope = high derivative
Process the signal with
  deriv_sq = (d(signal)/dt)2
  run_avg = running_avg_over_200ms (deriv_sq)
  then do the same peak detect + min/max/thresh + lockout as in track 1
Only declare QRS if both tracks have a peak above their threshold at the same time
Notes: The “running average over 200ms” is quite similar to the actual Pan-Tompkins algorithm. They say that its purpose is to deal with a noisy peak or a double peak in the QRS complex, and ensure that we don’t double-count it.

## Slide 13: PTC pros and cons
Pros
  The “PT” part has been tested for over 35 years
  Unknown how much commercial usage
Cons
  The “C” part was done with a looming deadline
  Hence, tested on only one ECG (Joel’s)
Will it work on yours? If not, you get to fix it 

## Slide 14: Tour of the code
Look at main.c for lab #7

## Slide 15: Block diagram
sample
filtered
peak_1
thresh_1
peak_2
thresh_2
deriv_2
deriv_sq_2
avg_200ms_2
biquad filter
peak detect
moving threshold
5-point derivative
square
running average
peak detect
moving threshold
input > thresh
input > thresh
!refractory
dual QRS

## Slide 16: Debug tricks so far
Single step in the debugger to examine variables, CSRs, …
Compare HAL with CMSIS CSRs to debug either
Pause in the debugger to find which infinite loop you’re stuck at
Instrument FreeRTOS for task-switch debugging
Save debug info into a data structure for later printout

## Slide 17: Debug challenges for lab 7
Your ECG varies beat to beat (especially during exercise); how do you debug an algorithm’s performance on constantly-changing data?
The code has lots of variables and not much visibility
Data points appear at 500 samples/second; how do you deal with this much data?
The data often makes more sense as a graph than a table of numbers – our host API is just a UART
Any ideas for how to deal with these?

## Slide 18: Beat-to-beat variability
Finding code bugs is hard if the input data keeps changing on you. Any ideas?
  Use a canned input sequence, repeated over and over, and driven out onto a DAC (you can view it on a scope)
  Or even use the canned input sequence directly as the ADC output
  Only move to a live ECG when you’re “fully debugged”

## Slide 19: Variables without visibility
So many variables: how do you see their relationships?
  for float or int variables: drive them out to a DAC
  for bool variables: drive them to a GPIO pin
  now you can look at them on a scope. Use two channels to view them superimposed on the original ECG
  you can even use four channels if you have them (we only have 2 DACs!)
  this gives you a graph capability

## Slide 20: The big Kahuna
Debug in single step on a desktop
  move the code to a host
  replace analog_read() with a function to grab one data point from the input data
  single step at your leisure
  full use of a host-based debugger
  can use your favorite graphing library to plot anything you want